Team 330 - NASA Jet Propulsion Laboratory; Raytheon; J&F Machine; and Hope Chapel Academy

Ability Chart:

| Goal Balancing | Ball Grabbing | Field Crossing | Bridge Tending | Other |
| --- | --- | --- | --- | --- |
| 2 goals w/robot | 2 Big Balls | Over Bridge | Arm Push Down | Slight goal lifting |

Notes:

- 4-wheel drive base with drill motors.

- Rotating “arm” powered with window motor (resembles turntable).

- “Forklift” to grab and deposit 2 big balls powered with Fisher-Price Motors.

- Spring-action “claws” to grab 2 goals (one on each side).

- Pneumatics lift goals slightly to transfer weight to wheels for balancing.

Comments:

________________________________________________________________

________________________________________________________________

________________________________________________________________

________________________________________________________________

# Text boxes

330

# Beach Bot 2001

## Beach Bot v4.0